## Slide 1: RD1 and related STAR FCS updates.
O.Tsai 07/18/2013

## Slide 2
Ramping up construction of three calorimeter prototypes at UCLA:
a) EIC barrel EMC Wpowder/ScFi
b) STAR forward EMC Wpowder/ScFi similar to one tested in 2012 for EIC.
c) STAR forward HCAL Pb/Sc.
All will use MPPC for readout. Design for readout FEE by IUCF/BNL groups.
Manpower at UCLA:
Two summer students (M.Sergeeva, UCLA and A. Lamson RPI). Postdoc (Xiaohua Liu UCLA).

## Slide 3
a) Status for EIC barrel EM prototype (tapered)
All components in hand (fibers, new meshes, etc.)
First version of molding form produced, currently tweaking it.
Light Mixer
Bundled Fibers
Inclined Meshes
Two towers, 18 X0 deep.

## Slide 4
More pictures of wedge assembly.
This area will be epoxied, first.
Then after final assembly cut along this line.
Individual light mixer for every
bunch of fibers (4 per tower).
4 MPPC per tower.
Design of light collection is driven
by requirement to get
500 p.e. /GeV.
May be overcomplicated.

## Slide 5
b) Status of forward EM for STAR.
All components in hand.
New 5 cm meshes with modified hole pattern along edges and smaller hole diameters and slightly smaller fiber to fiber distances compare to first prototype tested in 2012 were produced.
Molding form in production (much simple compare to tapered EIC form).

## Slide 6
c) HAD prototype.
Pb/Sc (10/2.5 mm), 4 Int. length
16 towers (10cm x 10cm).
Status:
a)All structural components produced.
b) Absorber plates scheduled for delivery in mid. August.
c) All scintillation plates (12” x12”) from EJ delivered. ~ 40% cut to final tile
dimensions (edges have not been polished yet on any of them).
d)All WLS plates form EJ delivered, no additional processing required.

## Slide 7
HAD optimization of light collection (M. Sergeeva)
WLS bar 852 mm x 97 mm x 3 mm.
Sc Tile, excited by 350 nm LED.
PMT with known QE at 490 nm.
Measure light collection for different:
Reflectors behind WLS bar
Reflectors surrounding Sc tiles
Reflectors at the end of WLS bar
Air gap thickness between Sc/WLS
Position of Sc tiles along the WLS bar
Find compensation scheme for light
collection along the WLS bar (need to
compensate about factor of two).
(With MPPC compensation may be different , need to run (e) again)
For optimal configuration compare readouts, PMT vs 8 MPPC.
Later with all Sc tiles in place and optimal configuration do cosmic to measure p.e./MeV

## Slide 8
MPPC Testing. (A. Lamson, Xiaohua Liu, with suggestions from Gerard V.(IUCF))
We just got from Hamamatsu 280 MPPC S10931-025P. For test run we’ll need 256.
Want to test Gain, PDE, Dark rate (TBD) vs bias for all of them. Temperature dependence for
few sensors only. Look at optimal bias settings for test run.
For simplicity decided to adopt 2D station to move light source. Designed test board for 16
channels. Tested Hamamatsu 410 nm laser (optical fiber with diffuser) and Blue LED with diffuser (Intensity profile and stability) – decided to proceed with laser.
Test board has 16 independent channels with preamps, mechanics to mount MPPCs,
Temperature sensors (I2C bus), interfaced with existing DAQ.

## Slide 9
How well mechanical mounting of MPPC work? It is not clear, need to try.
Boards have been produced and shipped yesterday to UCLA, in few days they will be populated
and then we’ll learn how well this scheme work.

## Slide 10
General:
Test run at FNAL Feb. 26 – March 18, right after sPHENIX – which is good as we’ll use their
beam tune up .
With delay of our test run we got a little bit more time to prepare, but not really too much,
because extra time we got is winter holidays and RHIC Run 14 startup.
So, the plan is the same as it was before – push and finish all prototypes early in the fall.
Thanks!